## Slide 1
// TECHNICAL PANEL · THERMAL FLUIDS
Design concepts for a marine PWR
A standardized two-loop plant, and the four ways a ship makes it harder than a site.
OCEAN ATOMICS
G. FREEMAN · B. HANSON · T. METZGER
2026-09-17
Notes: Open by naming the frame: this is a concept walkthrough, not a claim about your design. Twelve minutes, then questions.

## Slide 2
// THE FRAMING
A land plant is optimized. A ship plant is bounded by things that move.
GRAVITY
Direction and effective elevation change with heel and roll
HEAT SINK
Seawater from 0 to 32 °C, fouling, air ingestion in heavy seas
VOLUME
No tank farm, no unlimited elevation, no long pipe runs
ACCESS
Maintenance happens at sea or at one lifecycle yard, not on demand
Notes: The one idea to land: the marine problem is a plant whose boundary conditions move. Say it in one sentence and let it sit.

## Slide 3
// ARCHITECTURE
Four choices, each with one reason
Two loops
Pressurized primary, saturated secondary, seawater sink. No intermediate loop — PWR chemistry does not need one and mass is the binding constraint.
Integral layout
Steam generators and pressurizer inside the vessel. No large-bore primary piping means no large-break LOCA in the design basis.
Turbo-electric drive
Reactor holds steady load while the ship maneuvers, and the same plant drops into any nuclear-ready hull.
Forced flow, passive backup
Canned-motor pumps at power; a tall riser and elevated SG carry decay heat with nothing running.
Notes: Each choice gets a reason, and each reason is proven-technology or repeatability. Do not pitch novelty.

## Slide 4
// FLOW PATH — THREE LOOPS, THREE BARRIERS
Core to propeller
PRIMARY 12.5 MPa
Core · 277→310 °C
→
Riser
→
SG tube side
→
Canned RCP
↺
SECONDARY 4.5 MPa sat
SG shell · 258 °C
→
Separator
→
Turbine-generator
→
Condenser · 7 kPa
→
Feed pumps
↺
SEAWATER open cycle
Sea chest
→
Strainer
→
Circ pumps
→
Condenser tube side
→
Overboard
The SG tube wall is the second fission-product barrier. The condenser tube wall is the boundary against the sea. Both get continuous activity monitoring on the low-pressure side.
Notes: This is the whiteboard slide. Draw it in this order and name the pressure and temperature at each interface. Then stop and let them pick a branch.

## Slide 5
// HEAT BALANCE · 120 MWT CLASS
Two equations get you every flow rate
Core thermal power
120 MWt
Gross electric
38.0 MWe
Net to the bus
36.0 MWe
Primary flow
661 kg/s
Steam flow
60.3 kg/s
Condenser duty
82.0 MWt
Seawater flow
2.50 m³/s
METHOD
ṁ = Q / (cp ΔT) ṁ = Q / (hg − hfw)
cp ≈ 5.5 kJ/kg·K hot pressurized water, ΔT = 33 K primary. Δh ≈ 1,990 kJ/kg from 190 °C feedwater to saturated steam. Seawater at 8 K rise.
Notes: State assumptions before numbers. If they change the power rating, redo it live — that is the skill being tested.

## Slide 6
// CYCLE
30% net is the right answer, not a compromise
Saturated steam caps the top temperature near 258 °C. A wet expansion costs turbine efficiency and erodes blades. Condenser backpressure is hostage to seawater temperature. House load takes two points.
44%
Carnot limit, 258 °C source against a 20 °C sea
~32%
Real cycle with moisture losses and isentropic efficiency
30%
Net after pumps. Fuel is cheap; volume and availability are not
Notes: Do not apologize for 30%. Reframe the objective function: volume, mass, availability — not heat rate.

## Slide 7
// CORE THERMAL-HYDRAULICS
Three margins to protect
01 · FUEL CENTERLINE
Most of the ΔT is across the pellet and the pellet-clad gap. UO₂ conductivity falls with temperature and burnup, so the same linear heat rate runs hotter at end of life.
02 · CLADDING
1,204 °C peak in a design-basis LOCA, driven by oxidation kinetics, not melting. The gap closes with burnup, which helps thermally and hurts mechanically.
03 · BOILING CRISIS
Subcooled nucleate boiling is the design regime. Lose it and the wall coefficient collapses under a vapor blanket within seconds.
MDNBR = q"crit / q"local ≥ 1.30
Not physics — the aggregate of hot channel factors, correlation scatter, and instrument uncertainty carried at 95/95.
Notes: Three limits, and what erodes each. If they push, name the four protection inputs: power tilt, low flow, high inlet temperature, low pressure.

## Slide 8
// DECAY HEAT
Shut down is not cooled down
AFTER TRIP
FRACTION
120 MWT CORE
REMOVAL PATH
1 second
6.0%
7.2 MWt
Coolant thermal inertia, pump coastdown
1 minute
2.5%
3.0 MWt
Natural circulation, SG steaming to atmosphere
1 hour
1.3%
1.6 MWt
Passive condenser to an ambient pool
1 day
0.5%
600 kWt
Pool boil-off inventory sets the grace period
1 month
0.1%
120 kWt
Ambient losses through vessel and structure
The question is always the same: how long can the plant sit with no power, no operator, and no external water and stay inside cladding limits. On a ship, "no external water" is ironic and still true.
Notes: Rule of thumb: 7% at trip, factor of ten per time decade. The design question is always the unattended grace period.

## Slide 9
// WHAT THE SHIP DOES TO THE PLANT
Four thermal-fluids problems with no land analogue
ρ g β ΔT H — with g moving
Natural circulation driving head depends on gravity direction and effective elevation. A loop with margin upright can stall at 20° of list. Passive cooling has to be demonstrated at the worst credible inclination.
Period matching
Roll periods of 8 to 16 seconds sit close to loop transit times and to two-phase density-wave periods. The failure mode is resonant flow oscillation, not gradual degradation.
Every free surface lies
Pressurizer, SG downcomer, hotwell, feed tank — all measured by differential pressure, all biased by heel, trim, and acceleration. Level is a safety control input.
NPSH at the bottom of a heave
Suction static head cycles with motion. Available NPSH must be computed at the trough, not the mean. Feed pumps on near-saturated condensate are the exposed case.
Notes: This is the slide that differentiates you. Four items, in order of how much they worry you.

## Slide 10
// ULTIMATE HEAT SINK
The sink is free, infinite, and hostile
2.5 m³/s of seawater through the condenser at full power. That single number sizes the sea chest, the strainers, the circulating pumps, and the through-hull penetrations.
TEMPERATURE
0 to 32 °C across trade routes. Design warm and carry margin, or design mean and derate in the tropics.
FOULING
Biological growth and harbor silt. Fouling factor in the design UA, titanium tubing, cleaning access at the yard.
AIR INGESTION
Sea chest uncovering in heavy seas. Vacuum loss is a real cause of unplanned derating.
DISCHARGE
Thermal plume limits in port, and a permit conversation in every jurisdiction the ship calls at.
Notes: The heat sink is free and hostile. Name the tradeoff rather than picking a side.

## Slide 11
// WHAT I WOULD WANT TO ANALYZE FIRST
Five open questions
At what heel angle and sea state does the passive decay heat removal argument stop closing, and how much of that margin is analysis versus test?
Does roll excitation couple into density-wave instability in the riser, and does the current transient model resolve it?
Once-through or recirculating steam generator — is compactness or transient forgiveness the governing argument here?
What is the design seawater temperature, and is tropical derating accepted or engineered out?
Standardization is the strategy — where does it break, and what has to be re-analyzed per hull rather than per plant?
Notes: Close on questions, not conclusions. This signals you know the boundary of your own analysis and invites them into the technical conversation.

## Slide 12
// WHERE I FIT
Boiling limits, measured on hardware
Heat-pipe wicking is a critical heat flux problem: liquid delivery against vapor escape. Multiphase flow and desalination work is void fraction, flow regime, and fouling in real seawater. Same physics, different geometry.
CHF, EXPERIMENTALLY
Designed against a dryout limit on a rig, not just from a correlation
SEAWATER SERVICE
Evaporators, condensers, scaling and material selection in the real fluid
FIRST-OF-A-KIND
Comfortable where the requirement moves and the rig is the analysis
Notes: One sentence on fit, then hand it back to them. Do not oversell.